## Slide 1: Scenario and Data Summary

## Slide 2: Item #8: Silent failure scenario
Event: Service latency increases.
Cause: An application on the server froze and occupied the CPU. For example, if there were 4 CPUs, even if one of them was occupied, the CPU usage of the server being monitored was 25%, so it was not noticed.
Slow response?
Server
Application
Web servers
AP servers
DB servers
1. An application freezes and occupies one CPU.
2. Response to requests to this server becomes slow.
3. The server has 4 CPUs and one of them is occupied by the failure. It is only about 25% of the total CPU capacity, so no alert is generated.
4. Since there are many system components and no alerts are generated, it is difficult to manually investigate.

## Slide 3: Scenario Environment Diagram
Node (EC2)
User
Slow response?
Request from a user

## Slide 4: Scenario Environment Configuration
 | instance ID | Domain Name System | IP address
Web layer (React) | i-02f00924ea3138dcd | ip-10-1-100-128.ap-northeast-1.compute.internal | 10.1.100.128
 | i-0b90f7743e0a2fb26 | ip-10-1-12-176.ap-northeast-1.compute.internal | 10.1.12.176
 | i-03e386f9757915c39 | ip-10-1-12-70.ap-northeast-1.compute.internal | 10.1.12.70
 | i-0728626c32afef7b6 | ip-10-1-13-162.ap-northeast-1.compute.internal | 10.1.13.162
 | i-00406c791cac0970f | ip-10-1-13-87.ap-northeast-1.compute.internal | 10.1.13.87
AP layer (nodejs, express) | i-078923fb30cac1ede | ip-10-1-100-109.ap-northeast-1.compute.internal | 10.1.100.109
 | i-0706030196da936fe | ip-10-1-12-186.ap-northeast-1.compute.internal | 10.1.12.186
 | i-0d8a47a12fbcfdeb0 | ip-10-1-12-146.ap-northeast-1.compute.internal | 10.1.12.146
 | i-04a5da0032591b1f6 | ip-10-1-13-66.ap-northeast-1.compute.internal | 10.1.13.66
 | i-0353f28fecdaceba1 | ip-10-1-13-124.ap-northeast-1.compute.internal | 10.1.13.124
DB layer (mysql) | i-0537f73edc6fdf23f | ip-10-1-100-239.ap-northeast-1.compute.internal | 10.1.100.239
 | i-0d3e91c99eda5ad55 | ip-10-1-12-179.ap-northeast-1.compute.internal | 10.1.12.179
 | i-09635558c8a3f2e2f | ip-10-1-12-155.ap-northeast-1.compute.internal | 10.1.12.155
 | i-08daf583db41a60c0 | ip-10-1-13-238.ap-northeast-1.compute.internal | 10.1.13.238
 | i-07e793cdbf9799d40 | ip-10-1-13-174.ap-northeast-1.compute.internal | 10.1.13.174

## Slide 5: Scenario Environment Details
Environmental Information
  Usage environment
    AWS EC2
    Web services in a 3-tier web structure
  Number of Entities
    Web layer: 5 units
    AP layer: 5 units
    DB layer: 5 units
  Failure Target EC2 Instance
    ip-10-1-100-109.ap-northeast-1.compute.internal
  Root Cause Location
    One API (/api/cpu_stress/) has an infinite loop bug that occupies one of the four cpu's.
    Time of potential bug: 2024/01/24 03:10Z
*Because EKS is fully managed, there is no Master Node (managed by AWS).
  SLI
    Web service latency
  Failure time (time when SLI begins to be affected)
    2024-01-24 03:10:51Z (Time when the response time was once as large as 60s.)
  Time for people to notice the failure (assumed)
    2024-01-25 03:10Z

## Slide 6: Scenario Creation/Procedures
Measurement period: 2024/01/23 03:10Z ~ 2024/01/25 03:10Z (48 hours 00 minutes)
API bug occurrence time: 2024/01/24 03:10Z
Affected instance: ip-10-1-100-109.ap-northeast-1.compute.internal
Root cause: A latent bug in the API develops, increasing the cpu load on one of the four at some time, affecting the response time of the service.
KPI(SLI): Web server latency
Specific difficulty: The CPU load increases but only occupies one of the four CPU cores, so only about 25% of the total load at best, and is not caught by the monitoring settings. However, the API processing is running in a multi-process manner, which affects the processing.
creation procedure
Periodically send external user requests to the Web service.
After one day, the API for the potential bug assumption is thrown to one AP server, and one of the four CPUs is occupied by the process.
Latency using that AP server will increase.
KPI (SLI) will use JMeter.
All EC2 metrics (CPU usage, memory usage, etc.) are obtained from CloudWatch Metrics.
All EC2 logs are obtained from CloudWatch Logs.
From the data in 4~6, etc., identify the root cause related to SLI (CPU rise in ip-10-1-100-109.ap-northeast-1.compute.internal or API log).

## Slide 7: Scenario Creation/Procedures
Information that could be used to identify the cause
CPU increase. However, overall, it is 25% at the highest.
Increased latency & TimeOut when failure occurs
API Log
1706065851560,60004,scenario8_app_request,504,Gateway Time-out,scenario8_app_1_48h 1-857218,text,false,,292,193,3,3,http://internal- web-load-balancer-1126774120.ap-northeast-1.elb.amazonaws.com/api/sample_message,60004,0,2
2024-01-24T03:10:51.865Z [2024-01-24T03:10:51.510] [DEBUG] debug - API: /cpu_stress , Message: start
Web servers
AP servers
DB servers

## Slide 8: Stored Data Summary

## Slide 9: sampling data
KPI
  folder
    /KPI/JMeter/result/*.jtl
  JMeter Data
    Same as existing.
    HTTP status code is the data in the third column from the left (200, 200, 504 in the figure below)
      In addition to the time of the failure that occurred this time, there were a few 502 Bad Gateway errors, so the error rate seems to be difficult.
      504 If we look at Gateway Time-out only, we may be able to identify it since it occurs only at the time of failure.
    Latency is the data in the third column from the right (in the figure below, 200, 200, 503)
  Latency, error rate, utilization rate, etc. can be calculated from the above data and used as examples for multiple KPIs.
1706065911519,34,scenario8_app_request,200,OK,scenario8_app_1_48h 1-857816,text,true,,11748,193,3,3,http://internal-web-load- balancer-1126774120.ap-northeast-1.elb.amazonaws.com/api/sample_message,34,0,3
1706065911524,30,scenario8_app_request,200,OK,scenario8_app_1_48h 1-857817,text,true,,19664,193,3,3,http://internal-web-load- balancer-1126774120.ap-northeast-1.elb.amazonaws.com/api/sample_message,29,0,2
1706065851560,60004,scenario8_app_request,504,Gateway Time-out,scenario8_app_1_48h 1-857218,text,false,,292,193,3,3,http://internal- web-load-balancer-1126774120.ap-northeast-1.elb.amazonaws.com/api/sample_message,60004,0,2
...
column header | Description.
timeStamp | starting time
elapsed | Elapsed time (ms) from sending the request to the end of the response
responseCode | HTTP Response Code
threadName | JMeter thread name. If you don't use multiple thread groups, you can turn them off individually in configure because they are not very useful.
success | Whether results were returned for the request
bytes | bytes sent and received
grpThreads | Number of active threads in that thread group
allThreads | Total number of active threads for all thread groups
Latency | Elapsed time from sending out the request until the first byte returns (ms)
Table: Contents of JMeter

## Slide 10: sampling data
metrics
  folder
    /Metric/entity/
    Under the entity, the instance ID on page 4 is used as the folder name, and each entity is classified by entity.
  CloudWatch Metrics Data
    1 hour per file x 48 (2 days) with json files.
    There is information on 7 metrics in one file.
    The sample interval should be in 1 second increments.

## Slide 11: sampling data
metrics
  Data Contents
      Id: Metrics name
      Label: Label name
      Timestamp: Timestamp of the data point formatted in Unix timestamp format.
      Values: Data points of the metric corresponding to Timestamps, where Timestamps[x] is Values[x].
      StatusCode: Status of data returned. Complete indicates that all data points within the requested time range have been returned.
file-name | Contents
cpu_usage | cpu utilization. Unit: percent
memory_used | Memory utilization. Unit: percent
disk_used | Used disk space. Unit: bytes
diskio_reads | Number of disk read operations. Unit: counts
diskio_writes | Number of disk write operations. Unit: count
netstat_established | Number of established TCP connections. Unit: count
swap_used | Percentage of swap space currently in use. Unit: percent
Table: Types of Metrics
{
"MetricDataResults": [
{
"Id": "xxx",.
"Label": "xxx", "xxx".
"Timestamps": ["2024-01-25T03:09:59+00:00", ...],...
"Values": [1.005025125602533, ...],.
"StatusCode": "Complete"
}, }
{...}
]
}
Figure: Contents of json data

## Slide 12: sampling data
log
  folder
    /Log/
  CloudWatch Logs Data
    Logs of all entities are stored in text format: first column log time, second column log details.
    Data Type
      /messages: Log of all entities. General messages about the system are stored.
      /api_debug: Debug log of the AP layer, which contains messages when the API is executed.
      /mysql: mysql logs of DB layer, including connection logs to mysql, which user connected from which host, and what queries were executed.